Cuevas Kyllian
Mirbey Thomas

N-Lateration for Positioning Systems

The 3D N-Lateration Positioning System determines the position of a mobile device (represented in purple) by measuring distances from multiple access points. The system stores and processes data as follows:
Storage Mechanism:
- AccessPoint Class: Each access point has an ID, coordinates (x, y, z), a radius (distance to the mobile phone), and a color for visualization.
- List of AccessPoint Objects: A list stores all reference access points used for positioning.
- Estimated Position (trilaterate function output): The estimated (x, y, z) coordinates of the mobile phone.
Processing Flow:
1. Distance Calculation:
  1. The system uses the Euclidean distance formula to compare actual and estimated distances.
  2. The difference between measured (radius) and computed distances is used as the error metric.
2. Optimization with minimize():
  1. The trilaterate function minimizes the error function (calculate_error) to find the most likely phone position.
  2. The optimization algorithm iteratively adjusts (x, y, z) to minimize the sum of squared distance errors.
3. Visualization (draw function):
  1. The 3D plot shows access points as spheres and the estimated position as a cross.
  2. The plot dynamically adjusts limits based on access point positions.

2. Implementation Details
2.1 Computing Distance Errors
- Each access point's actual distance (radius) is compared with the calculated distance from an estimated phone position.
- The squared error is computed as:

This error is minimized using the SciPy minimize() function.
2.2 Finding the Best Position (Trilateration)
- The function trilaterate() finds the (x, y, z) position by minimizing calculate_error().
- The initial guess is (0,0,0), and the optimizer iteratively refines the estimate.
2.3 Visualization (3D Plot)
- The draw() function creates a 3D scatter plot:
  - Spheres: Represent access points.
  - Crosses: Indicate the estimated phone position.
  - Color Coding: Differentiates access points.
2.4 Main Execution
- The script initializes access points with known positions and distances.
- It computes the estimated phone position (trilaterate).
- The estimated position is printed and plotted in 3D.

3. Results and Analysis
- The estimated phone position depends on:
  - The accuracy of RSS measurements.
  - The number and placement of access points.
- The method balances computational efficiency and accuracy.
- Future improvements may include refining weight functions or filtering noisy signals.

5. Code Overview
The implementation consists of the following key functions:
- calculate_error() – Computes the squared error between measured and calculated distances.
- trilaterate() – Uses optimization to find the best (x, y, z) position.
- draw() – Visualizes access points and estimated phone position.
- AccessPoint class – Stores access point information and provides a method to draw spheres.
6. Diagrams and Figures
Class Diagram:

Flowchart:

Interaction diagram:
1
2
3
4
5
6
7